## Slide 1
Snort IDS
pfSense FW
Wazuh SIEM
DAM PLC
Securing Industrial
Control Systems
Real-Time Attack Detection Using Snort IDS & Wazuh SIEM
Modbus TCP · Snort IDS · pfSense · Wazuh SIEM · MITRE ATT&CK for ICS
CYB691 · Spring 2026
Notes: SLIDE 1 — OPENING Greet the audience and set the scene immediately. Don't waste time on logistics. Today I want to show you something that most enterprise security teams completely overlook — the networks that run our physical world. Power grids, water treatment plants, manufacturing floors — all running on protocols designed decades ago with zero security in mind. My project, the NYMEGA ICS Cyber Range, simulates exactly those environments and shows how we can detect attacks against them in real time."

## Slide 2
Detection Gaps in ICS Environments
No Protocol Visibility
Traditional firewalls allow Modbus TCP through without inspecting function codes — any FC16 write looks identical to legitimate traffic.
No Authentication
Modbus has zero built-in authentication. Any device on the network can issue write commands to a PLC with no credentials required.
No SIEM Correlation
IDS alerts existed in isolation. Without SIEM forwarding, there was no way to correlate events, count frequency, or trigger automated responses.
No MITRE Mapping
Alerts had no threat context. Without ATT&CK for ICS mapping, defenders couldn't classify attacks by tactic or technique.
Notes: SLIDE 2 — DETECTION GAPS This is your "problem statement" slide. Establish WHY this project matters before showing what you built. SAY: "Before I show you the solution, let me walk you through why ICS environments are so difficult to protect. There are four fundamental gaps that most organizations ignore completely." WALK THROUGH EACH CARD: 1. NO PROTOCOL VISIBILITY — "A standard firewall sees Modbus TCP traffic and just lets it through. It has no idea whether that packet is a legitimate read or an attacker rewriting PLC registers. Function codes are invisible to it." 2. NO AUTHENTICATION — "Modbus was designed in 1979. There is literally no username, no password, no certificate. If you're on the network, you can command any PLC. That's the threat model we're dealing with." 3. NO SIEM CORRELATION — "Even if Snort generates an alert, without forwarding to a SIEM you have no way to correlate events, spot patterns, or trigger responses. Alerts die in a log file no one reads." 4. NO MITRE MAPPING — "Security teams speak MITRE ATT&CK. ICS attacks need their own framework — ATT&CK for ICS — and most SIEM platforms don't include it by default." TRANSITION: "These are the four gaps my pipeline addresses. Let me show you the environment I built to test and validate it."

## Slide 3
Environment Architecture
Kali Attacker
10.13.20.21
Attack Simulation
pfSense + Snort
10.13.20.240
IDS / Firewall Gateway
Wazuh SIEM
10.13.20.17
Alert Correlation
DAM PLC
10.14.6.10
Target OT Device
Modbus TCP
Port 1502
Syslog UDP 514
OT Network
10.14.6.0/24
IT / Corporate Network — 10.13.20.0/24
OT Field Network — 10.14.6.0/24
Notes: SLIDE 3 — ENVIRONMENT ARCHITECTURE SAY: "This is the NYMEGA ICS Cyber Range — four virtual machines, two network segments, simulating a real OT environment." POINT TO EACH NODE: - KALI (10.13.20.21): "This is our attacker — a Kali Linux machine simulating a threat actor who has gained access to the corporate network and is attempting to pivot into the OT segment." - pfSense (10.13.20.240): "This is our ICS gateway — pfSense firewall running Snort IDS on the vtnet3 interface, inspecting all traffic destined for the OT network." - Wazuh (10.13.20.17): "This is our SIEM — Wazuh 4.5.2 receiving Snort alerts via syslog on UDP 514, correlating events and generating classified alerts." - DAM PLC (10.14.6.10): "This is the target — a simulated Programmable Logic Controller representing a dam water flow control system, listening on Modbus TCP port 1502." EXPLAIN NETWORK SEGMENTS: "Notice the two distinct networks — 10.13.20.0/24 is the IT network where our attacker lives, and 10.14.6.0/24 is the isolated OT field network. The pfSense firewall sits between them, which is where Snort does its inspection."

## Slide 4
The Detection Pipeline
1
Attack Executed
mbpoll sends Modbus TCP
to PLC port 1502
→
2
Snort Detects
Custom rules match
FC03/FC06/FC16 payload
→
3
Syslog Forwarded
pfSense sends alert
to Wazuh UDP 514
→
4
Wazuh Decodes
snort decoder matches
prematch snort[
→
5
Rule Fires
100501/100502/100510
/100530 alert generated
# Full Pipeline Flow mbpoll -m tcp -p 1502 10.14.6.10 → Snort Alert → pfSense Syslog UDP:514
Wazuh Decoder (snort[) → Rule Match → alerts.json + MITRE ATT&CK for ICS
Notes: SLIDE 4 — DETECTION PIPELINE This is the technical heart of your presentation. Walk through each step clearly and slowly. SAY: "Let me walk you through exactly how an attack travels through this pipeline from execution to SIEM alert." STEP BY STEP: 1. ATTACK EXECUTED — "The attacker runs mbpoll — a command-line Modbus TCP client — sending a write command to the PLC on port 1502. This is a real tool used in legitimate ICS testing, and it's exactly what an attacker would use." 2. SNORT DETECTS — "Snort on pfSense intercepts the packet. Our custom rule inspects the Modbus Application Protocol header — specifically the function code byte at offset 7. If it matches FC03, FC06, or FC16, Snort fires an alert." 3. SYSLOG FORWARDED — "pfSense is configured to forward Snort alerts to Wazuh via UDP syslog on port 514. This is the bridge between the IDS and the SIEM." 4. WAZUH DECODES — "Wazuh receives the syslog message and runs it through our custom decoder. The prematch 'snort[' identifies it as a Snort alert, and the child decoder snort-modbus confirms it contains MODBUS in the message." 5. RULE FIRES — "The matching rule fires — 100501 for FC16, 100502 for FC06, 100510 for FC03, or 100530 for DoS — and the alert is written to alerts.json with severity level and MITRE technique ID." POINT AT CODE: "The full pipeline in one line — mbpoll to Snort alert to pfSense syslog to Wazuh decoder to rule match to alerts.json." KEY INSIGHT: "The whole chain happens in under a second. From attack to SIEM alert — real time detection."

## Slide 5
Four Attack Scenarios
01
FC03
Read Reconnaissance
T0846 — Remote System Discovery
Rule: 100510 L7
Tactic: Discovery
✓ DETECTED
02
FC06
Single Register Write
T0831 — Manipulation of Control
Rule: 100502 L10
Tactic: Impair Process
✓ DETECTED
03
FC16
Multi-Register Write
T0831 — Manipulation of Control
Rule: 100501 L12
Tactic: Impair Process
✓ DETECTED
04
FLOOD
DoS / Flood Attack
T0814 — Denial of Service
Rule: 100530 L13
Tactic: Inhibit Response
✓ DETECTED
Notes: SLIDE 5 — FOUR ATTACKS OVERVIEW SAY: "I executed four attacks against this environment, designed to simulate a realistic attacker progression — from quiet reconnaissance all the way to destroying availability. Let me walk you through each one." 01 — RECON: "First they look. FC03 reads registers silently. The attacker is mapping the process — what values are where, what setpoints are active, what the normal state looks like. This is intelligence gathering." 02 — PROBE: "Then they test. FC06 writes one value to one register. Small, targeted, hard to notice. They're verifying they have write access and seeing if anyone notices a small change." 03 — TAKEOVER: "Then they act. FC16 rewrites multiple registers simultaneously — setpoints, control values, safety thresholds — all at once. This is the moment of compromise." 04 — DESTRUCTION: "And if they want to prevent response, they flood the PLC. Hundreds of requests per minute. The PLC can't process legitimate operator commands anymore. Emergency shutdowns don't execute."

## Slide 6
MITRE ATT&CK for ICS Mapping
Attack
FC Code
MITRE ID
Technique Name
Tactic
Rule / Level
Recon
FC03
T0846
Remote System Discovery
Discovery
100510 / L7
Write Single
FC06
T0831
Manipulation of Control
Impair Process
100502 / L10
Write Multi
FC16
T0831
Manipulation of Control
Impair Process
100501 / L12
DoS Flood
FC06 x10+
T0814
Denial of Service
Inhibit Response
100530 / L13
ATT&CK for ICS Tactics Covered
Discovery
Enumerate PLC state
and register values
Impair Process
Control
Manipulate register
values and setpoints
Inhibit Response
Function
Flood PLC to prevent
legitimate commands
Notes: SLIDE 10 — MITRE ATT&CK FOR ICS MAPPING This slide shows the academic and professional rigor of your work. It's what separates your project from "I set up Snort" to "I built a classified threat detection system." SAY: "Every alert our pipeline generates is mapped to the MITRE ATT&CK for ICS framework. This matters because it gives defenders shared language and threat context." WALK THE TABLE: - "FC03 maps to T0846 — Remote System Discovery under the Discovery tactic. The attacker is learning the environment before they strike." - "FC06 and FC16 both map to T0831 — Manipulation of Control under Impair Process Control. One register or many, the intent is the same — change what the PLC believes it should be doing." - "The DoS flood maps to T0814 under Inhibit Response Function. The goal isn't manipulation anymore — it's preventing any response at all." EXPLAIN THE CHALLENGE YOU OVERCAME: "Here's something important — Wazuh 4.5.2 does not include MITRE ATT&CK for ICS techniques out of the box. The T08xx technique range simply doesn't exist in the default database. I had to inject them manually into Wazuh's SQLite mitre.db using Python. That's not documented anywhere — I had to figure that out." POINT TO THREE TACTICS: "Three distinct tactics covered: Discovery, Impair Process Control, and Inhibit Response Function. These map to the pre-attack, attack, and denial phases of the kill chain." IF ASKED about other ATT&CK for ICS techniques: "The full ICS framework covers 12 tactics and over 80 techniques. Our pipeline covers the most common Modbus attack patterns. Future work would expand to cover DNP3, EtherNet/IP, and additional function codes."

## Slide 7
Detection Gaps Fixed by This Pipeline
✗
No Modbus Protocol Visibility
✓
Custom Snort rules inspect FC byte in Modbus MBAP header — detecting FC03, FC06, FC16 at the packet level
✗
No SIEM Correlation
✓
pfSense syslog forwarding to Wazuh via UDP 514, custom decoder chain, hierarchical rule set with if_sid parent-child logic
✗
No Frequency-Based DoS Detection
✓
Wazuh frequency rule 100530 triggers after 10 FC06 alerts in 60 seconds using if_matched_sid correlation
✗
No MITRE ATT&CK for ICS Context
✓
T0831, T0814, T0846 injected into Wazuh mitre.db — all rules now carry ICS technique and tactic labels
Notes: SLIDE 11 — DETECTION GAPS FIXED This is your "before and after" slide. It directly answers the question: what problem did you actually solve? SAY: "Let me be direct about what this pipeline changes. For each of the four gaps I showed you at the start, here's exactly what we built to close it." WALK EACH ROW: 1. PROTOCOL VISIBILITY: "Before — firewalls saw Modbus as generic TCP and let it through. After — Snort rules inspect the MBAP header and function code byte at the packet level. FC03, FC06, and FC16 are now individually detectable, not just 'Modbus traffic.'" 2. SIEM CORRELATION: "Before — Snort alerts existed in isolation on pfSense, visible only to someone SSH'd into the firewall. After — every alert is forwarded via syslog to Wazuh, decoded by our custom decoder chain, matched against hierarchical rules, and stored in alerts.json with full metadata." 3. FREQUENCY-BASED DOS DETECTION: "Before — a flood of write requests looked identical to normal traffic at high volume. After — Rule 100530 uses Wazuh's frequency correlation engine to count events over time. Ten FC06 alerts in 60 seconds is statistically abnormal and triggers a Level 13 DoS alert." 4. MITRE ATT&CK FOR ICS: "Before — alerts had no threat classification. An analyst seeing a Snort alert for Modbus had no framework to interpret it. After — every alert carries a MITRE technique ID and tactic. T0831 tells a defender immediately: this is Manipulation of Control, Impair Process Control tactic."

## Slide 8
Results Summary
4
Attacks
Executed
4
Attacks
Detected
100%
Detection
Rate
3
MITRE ICS
Techniques
Attack Type
FC Code
Rule
MITRE Technique
Tactic
Detected
FC03 Read Recon
FC03
100510 L7
T0846 Remote Discovery
Discovery
✓
FC06 Single Write
FC06
100502 L10
T0831 Manip. of Control
Impair Process
✓
FC16 Multi Write
FC16
100501 L12
T0831 Manip. of Control
Impair Process
✓
Modbus DoS Flood
FC06+
100530 L13
T0814 Denial of Service
Inhibit Response
✓
All 4 attack scenarios detected in real-time — 0 false negatives
Notes: SLIDE 12 — RESULTS SUMMARY Simple, confident delivery. Let the numbers speak. Don't over-explain. SAY: "The results are simple. Four attacks executed. Four attacks detected. One hundred percent detection rate. Zero false negatives across every test run." POINT TO THE STATS: "4 attacks executed — FC03 recon, FC06 single write, FC16 multi-write, and Modbus DoS flood. All deliberate, all using real tools an attacker would use." "4 attacks detected — every single one caught by the pipeline before it could persist unnoticed." "100% detection rate — not a single attack slipped through." "3 MITRE ICS techniques covered — T0831, T0814, T0846 — spanning three distinct attack tactics." WALK THE TABLE QUICKLY: "FC03 recon — Rule 100510, Level 7, T0846, detected. FC06 write — 100502, Level 10, T0831, detected. FC16 write — 100501, Level 12, T0831, detected. DoS flood — 100530, Level 13, T0814, detected." CLOSE THE SLIDE: "No attack went undetected. That's the headline. The bottom line of this entire project." IF ASKED about false positives: "We focused on validating detection — false positive tuning would be the next step in a production deployment. The severity levels and specific match patterns are designed to minimize noise, but production tuning would require baseline traffic analysis."

## Slide 9
Conclusion
What This Pipeline Achieves
✓
End-to-end ICS attack detection — from Modbus TCP packet to SIEM alert in real time
✓
Custom Snort rules detect unauthorized Modbus FC03, FC06, and FC16 function codes at the packet level
✓
Wazuh hierarchical rule chain (100500–100530) classifies attacks by type and escalating severity
✓
MITRE ATT&CK for ICS mapping provides threat context: T0831, T0814, T0846 — discovery to control disruption
✓
Frequency-based correlation (Rule 100530) detects Modbus flood / DoS at Level 13 — the highest severity
✓
100% detection rate — all 4 attacks detected with 0 false negatives across every test run
Notes: SLIDE 13 — CONCLUSION Your closing. Be direct, be proud of what you built, and leave them with the one sentence that summarizes everything. SAY: "Let me close with what this pipeline actually achieves." READ THROUGH THE LIST WITH BRIEF COMMENTARY: - "End-to-end detection — from the moment mbpoll sends a Modbus packet to the moment Wazuh generates a classified alert. Real time." - "Custom Snort rules — these don't exist in any default ruleset. I wrote them specifically for Modbus function code detection." - "Hierarchical Wazuh rules — 100500 as the parent, children refining by function code. This is the correct architecture. Without it, one rule swallows everything." - "MITRE ATT&CK for ICS — manually injected into Wazuh's database because it's not there by default. That's a gap in the tool that I identified and fixed." - "Frequency-based DoS detection — behavioral correlation, not just signature matching. This is the difference between detecting an individual packet and detecting an attack pattern." - PAUSE on the green row — "100% detection rate. Every attack caught. Zero missed. That's what this system delivers." CLOSING LINE — say this slowly and clearly: "No Modbus attack went undetected — reconnaissance, manipulation, full control takeover, and denial of service — all caught in real time." THEN OPEN FOR QUESTIONS: "I'm happy to walk through any part of the technical implementation, the rule logic, the decoder configuration, or the MITRE mapping in detail." ANTICIPATED QUESTIONS TO PREPARE FOR: - Why Wazuh and not Splunk/Elastic? - How would this scale to a real production OT environment? - What about encrypted Modbus or other ICS protocols? - How did you handle the pfSense syslog format issues? - What's the performance impact of Snort on the firewall?